SPECIFICATIONS FOR INSITEIG DISSOLVED OXYGEN SENSOR

The fluorescent Dissolved Oxygen sensor shall be a type that does not require replaceable sensor caps, membranes, cartridges, or fill solutions as these types of designs are not acceptable. The sensor shall not be damaged by exposure to direct or indirect sunlight nor will exposure to sunlight affect the calibration.

The dissolved oxygen sensor will have a five year warranty and will not require any consumable or spare parts during this period with normal field deployment.

Specific dissolved oxygen sensor requirements in addition to the above are:

- Measuring Range: 0 to 25 ppm

- Accuracy: 1% of the reading or .05 ppm, whichever is greater

- Repeatability: 0.01 ppm

- Response Time: 95% in under 60 seconds

- Resolution: 0.01 ppm below 4.00, 0.1 ppm above 4.0

- Drift: less than 1% per year

- Temp. Range: 0°C to 60°C

- 1-½" MNPT mounting thread

- 33ft (10m) sensor cable standard – custom on request

- ¼" O.D. tube connection for jet cleaning