SPECIFICATIONS FOR INSITEIG ORP SENSOR

The ORP electrode will be a flat glass type of electrode. The ORP holder will have a built-in self-cleaning port to allow for air or water jet cleaning. No holder requiring external tubes or fittings to implement self cleaning will be accepted.

Specific ORP sensor requirements in addition to the above are:

- Measuring Range: +/- 2000mV

- Temp. Range: 10°C to 60°C

- 1-½" MNPT mounting thread

- 33ft (10m) sensor cable – custom lengths available

- ¼" O.D. tube connection for jet cleaning